Worksheet

Proposed meeting:-

- Richard Vere-Compton (R.V.C.), Managing Director of Dualeffort Ltd.

- Rory Bedeau (R.B.) of 19b, Woodhurst Road, Acton, London, W3 6SS.

Alhambra House, 27-31 Charing Cross Road, London, WC2H 0AU at 12noon – 1pm on Thursday 22 January 2004

R.V.C. will thank R.B. for his concept, which has lead to a viable interpretation of a storage device with a holding title of a Manual Storage Energy Module (M.E.S.M.).

R.V.C. will display a 17” Crossbow Prod (which is used in a Pistol X Bows type commando by Barnett International Ltd.).

Claims for M.E.S.M. :

- An energy storage system/product according to the present invention, where identical 17” crossbow prods, where put4 to the left and 4 to the right so that a hydraulic actuator could pull back 600lb, held as stored energy.

- A mechanism according to the present invention, where stored energy would be discharged in 30-60 seconds.

2a) This discharge would be through a mechanism known as Archimedes Return Screw.

2b) The mechanism, screw cut, would run at 500 R.P.M. plus.

2c) At 500 R.P.M. a military spec. alternator would generate 500 watts of electrical power at 75 volts. (A.C.).

- A mechanism according to the present invention, where a young child, 10years old+, could, through a hydraulic pump, which is fitted with a long reach handle, move the handle up and down (in a to-and-fro pump action).

3a) A mechanism which would be a hydraulic actuator, as in 1).

The signatures to this worksheet agree to work towards a common goal of a joint partnership, to produce a product which would have both patent and copyright protection.

With the said protection in place the M.E.S.M. will be offered to charities, whose specific aim is to put low-tech. solutions to hi-tech. problems in the hands of the worlds disenfranchised masses and, by the use of muscle power only, produce useable amounts of electrical energy to subsistence farmers, and thus raise their level of income, as they add a small sub-contract manufacturing capability to their farming skills.

This meeting concluded at 1300hrs, with both parties taking these notes with them, which were duly signed off and witnessed.